## Slide 1: MIPS processor Simulator including Tomasulo
Team 2: Junfei Wang, Jianyun Miao, Nengxing Shen

## Slide 2: Tomasulo’s algorithm
Presentor: Nengxing Shen

## Slide 3: Tomasulo’s algorithm
Tomasulo's algorithm is a computer architecture hardware algorithm for dynamic scheduling of instructions that allows out-of-order execution and enables more efficient use of multiple execution units.
The major innovations of Tomasulo’s algorithm include register renaming in hardware, reservation stations for all execution units, and a common data bus (CDB) on which computed values broadcast to all reservation stations that may need them.

## Slide 5
Reservation Station(RS): Functional Unit with its own buffers and its own local control.
Reservation station in Intel's Nehalem microarchitecture
Reservation Stations

## Slide 6
The Common Data Bus (CDB) connects reservation stations directly to functional units.
Common Data Bus

## Slide 7
Reigister Renaming
Register renaming is a form of pipelining that deals with data dependences between instructions by renaming their register operands.

## Slide 8: multi-issue
Presentor: Jianyun Miao

## Slide 9: Machine Parallelism

## Slide 10
Simple Superscalar pipeline
With multiple execution parts ( pipelined )

## Slide 11: five approaches

## Slide 12
Superscalar
  Issue a varying number of instructions per clock cycle
  Either statically scheduled by the compiler
  Or dynamically scheduled by the hardware
  using out-of-order execution(techniques like scoreboard, tomasulo)
VLIW
  Issue a fixed number of instructions formatted either as
  Inherently statically scheduled by the compiler

## Slide 13: Superscalar vs. VLIW
Superscalar
  Smaller code size
  Good binary compatibility
VLIW
  Simple hardware design for decoding and firing instructions
  Need to access more registers, typically using multiple register files

## Slide 14: problem of multi-issue
If Integer and FP operations are easily distinguishable combinations, then for such programs the ideal CPI = 0.5 if the following conditions are met:
  50% of the program is FP operation
  no correlation
If more commands are emitted at the same moment, the more difficult it is to decode and emit
VLIW
  Longer instruction words can accommodate more operations
  By definition, all operations in VLIW are combined at compile time and are independent of each other, i.e., they can be executed in parallel
  For example,2 int operations，2 float ， 2 memory references, 1 branch instruction
  use compilation technique scheduling to solve branching

## Slide 15: DEMO
Presentor: Junfei Wang